- 1 -

MATERIAL SAFETY DATA SHEET

OSTREM CHEMICAL CO. LTD.			Phone:  (780) 440-1911

2310 - 80 AVENUE			In Case of Emergency Only:

EDMONTON AB  T6P 1N2			Phone CANUTEC:  (613) 996-6666

Date completed:  Oct. 1, 2008

# PRODUCT NAME: 		I-8 BLEACH			CODE:  L511

OTHER NAME:

DISTRIBUTED BY:

WHMIS CLASSIFICATION:	C; E

TDG CLASSIFICATION:	Not Regulated

# HAZARDOUS INGREDIENTS	%WT/WT	CAS NO.		TOXICITY DATA

# (LD50 & LC50)

Sodium Dichloroisocyanurate	10-30	51580-86-0		LD50 Oral (rat) 735 mg/kg

Dihydrate (providing 8% available chlorine)				LD50 Dermal (rabbit) > 2 g/kg

PHYSICAL DATA FOR PRODUCT

Physical State:  White Solid	Sp. Gravity:   Not Avail.			pH: 1% Sol. 6-6.5

Boiling Point:  N/A	Vapour Pressure:   N/A

Vapour Density: N/A	Evaporation Rate:  N/A

Freezing Point:  N/A

Solubility in Water:  29 %

Appearance & Odour:  White granular powder with chlorine odour.

FIRE AND EXPLOSION DATA FOR PRODUCT

Flash Point (Test Method):  N/A

Flammable Limits in Air, % by vol. Non-flammable  Lower: N/A   Upper: N/A

Fire Extinguishing Substances:  ( ) Water Fog  ( ) Foam  (X) CO2

(X) Dry Chem  ( ) Other:  Water should only be used in flooding amounts.

Hazardous Combustion Products:	When heated to decomposition, emits carbon monoxide and

chlorine fumes.

Special Firefighting Procedures:  Wear suitable protective clothing and self-contained breathing apparatus.

REACTIVITY DATA FOR PRODUCT

Incompatibility:  ( ) Water  (X) Oxidizing Material  (X) Acid  (X) Base

( ) Other:  Should not be mixed with reducing agents, ammonia, ammonium compounds, amines, oil and grease.

Hazardous Decomposition Products:  Carbon dioxide, nitrogen trichloride, chlorine and cyanic acid.

Chemical Stability:   Stable at temperatures under 250oC

*N/A - Not applicable.

- 2 -

Product Name: 	I-8 BLEACH

HEALTH HAZARD INFORMATION FOR PRODUCT

EMERGENCY and FIRST AID PROCEDURES

Inhalation:	Get fresh air.  Call a physician.

Ingestion:	Immediately drink large quantities of water.  Do not induce vomiting.  Get medical attention.

Eyes:	Flush with cold water for at least 15 minutes.  Get medical attention.

Skin:	Flush thoroughly with cold water.

EFFECTS OF OVEREXPOSURE (Acute and Chronic)

Inhalation:	Severe irritation to respiratory tract.

Ingestion:	May cause severe throat and gastrointestinal irritation.

Eyes:	May cause severe irritation and possibly burns.

Skin:	May cause irritation.

PREVENTIVE MEASURES

Steps to be taken upon release or spillage (including neutralizing):

Minor spills should be washed down with lots of water and flushed to sewer.

Waste disposal method:

Discard to licensed dump in area free of organic matter, rubbish, etc.  Cover with soil.

Follow local, provincial and federal regulations.

Handling and Storage Requirements:

Store in cool, dry place away from nitrogen containing compounds and

other organic materials.  Keep in tightly closed container.  Protect from moisture.

Ventilation Requirements (Local or General):

Use in well ventilated area.

Respiratory Protection:

A dust mask should be worn.

Eye Protection:

Chemical Workers goggles.

Other Protection:

Gloves and coveralls should be worn.

Prepared by: Technical Services Department, Ostrem Chemical Co. Ltd., Ph: (780) 440-1911